FACULTY OF SCIENCE & TECHNOLOGY

Mining and Mineral Processing Department

COAL MINING METHODS, HMIE 325

### SESSIONAL EXAMINATION

DECEMBER 2016

DURATION:   3 HOURS

EXAMINER: MR. T. NYAMAGUDZA

Question1

- A 2.2 m thick coal seam located at a depth of 200 m is to be mined by room and pillar method. The designed rooms span is 7.5 m. Compute the pillar width and areal percentage extraction if the safety factor is 1.8.		[8]

- Explain the Inverse distance method of coal reserves estimation.		[6]

- Discuss the three forms of methane contact with rocks.				[6]

Question 2

- Briefly explain coal formation and ranking.							[8]

- Discuss at least FOUR open cut mining systems in terms of equipment working combinations in relation to seam. 							[8]

- Explain value addition to coal products locally and globally.		[6]

Question 3

- A dragline is required to remove 300 000 m3 of coal per month the bank volume basis considering it is required to work effectively 450 hours per month with a bucket fill factor of 0.8, cycle time 65 seconds and Swell factor of 1.25.

Compute the required bucket capacity of the dragline in cubic meters. [8]

- What are the main parts of a continuous miner and describe its application																					[6]

- Discuss the role of Shovels and Surface Miners in surface coal mining.	[4]

- Discuss briefly the variations of the room and pillar coal mining in terms of the production cycle.														[4]

Question 4

- Discuss the following properties of coal and how they affect the quality of coal;

  - Ash content

  - Fived Carbon

  - Volatile matter	    											[6]

- With the aid of diagrams, discuss the preproduction work for Longwall Mining system and also the cross-sectional layout of coal production equipment.															 		[10]

- Explain the purpose of ventilation survey in underground coal mines. 	[4]

Question 5

- State and explain the two longwall mining approaches / techniques	[4]

- State and briefly discuss four types of underground coal mine entry.	[4]

- Explain the term coal bed methane (CBM) and any two underground degassing methods.														[8]

- Discuss the measures for preventing methane explosions in underground coal mines.																	[4]

END OF QUESTION PAPER

# Text boxes

#### MIDLANDS STATE UNIVERSITY

## INSTRUCTIONS

- Answer all Questions

- Total marks 100

- All questions carry equal marks